## Slide 1: New Efficient Hardware Design for Batch Normalization Based on Convolution Neural Network Training
Student: Yu-Fan Teng, Yu-Sheng Ting
Advisor: Prof. Tzi-Dar Chiueh
National Taiwan University, Taipei, Taiwan
July 11, 2020

## Slide 2: Introduction
CNN has been a widely-used technique in deep learning
However, much fewer works focused on accelerating non-convolutional layers
  Batch Normalization (BN)
Most past works focused on the inference process only

## Slide 3: Introduction
For example: Bactran

## Slide 4: Background – Forward Process
Normalization
Scaling

## Slide 5
The gradient of the weights
The gradient of the inputs

## Slide 6: Overall Architecture
Overall Architecture
PE array
BN_processor
SRAM

## Slide 7: Forward/Backward Stage 1
Use the same circuit
Overall Architecture

## Slide 8: Forward/Backward Stage 1
Use the same circuit
  Forward
4 blocks for 4 output channel

## Slide 9: Forward Stage 2
Forward Stage 2
Two blocks
  Calculating mean, 1/sigma
  Calculating x_norm for backward

## Slide 10: Forward Stage 2
Forward Stage 2
Two blocks
  Calculating mean, 1/sigma
  Calculating x_norm for backward

## Slide 11: Forward/Backward Stage 1
Use the same circuit
  Backward
Forward/Backward Stage 1
∂y
∂ß/N
∂γ/N
4 blocks for 4 output channel

## Slide 12: Backward Stage 2
Backward Stage 2
Calculating partial_x

## Slide 13: Result
Timing Analysis
  Consider forward…
  Cycle spent in Stage 1
  Cycle spent in Stage 2
  Balanced condition: = 16
Result

## Slide 14
APR Result
Technology | UMC 0.18um Mixed-Mode and RFCMOS 1.8V/3.3V
IP size (m2) | 2000.12 x 1999.76
Gate Count | 1.41M
Power Supply | 3.3V
Frequency | 4.17MHz
Power | 140.87mW
Technology | UMC 0.18um Mixed-Mode and RFCMOS 1.8V/3.3V
 | 2000.12 x 1999.76
Gate Count | 1.41M
Power Supply | 3.3V
Frequency | 4.17MHz
Power | 140.87mW
Result

## Slide 15
Comparisons with other works
 | BNRELU | L1-Norm BN | Bactran | Our design
Supported operation | Inference only | Training and Inference | Training and Inference | Training and Inference
Interaction with convolution layer | - | No | Yes | Yes
Hardware resources sharing | - | No | No | Yes
power | - | - | 8.95W | 0.14W
Result

## Slide 16: Reference
[1] ZHANG, Chen, et al. Optimizing fpga-based accelerator design for deep convolutional neural networks. In: Proceedings of the 2015 ACM/SIGDA international symposium on field-programmable gate arrays. 2015. p. 161-170.
[2] CHEN, Yu-Hsin, et al. Eyeriss: An energy-efficient reconfigurable accelerator for deep convolutional neural networks. IEEE journal of solid-state circuits, 2016, 52.1: 127-138.
[3] ALWANI, Manoj, et al. Fused-layer CNN accelerators. In: 2016 49th Annual IEEE/ACM International Symposium on Microarchitecture (MICRO). IEEE, 2016. p. 1-12.
[4] IOFFE, Sergey; SZEGEDY, Christian. Batch normalization: Accelerating deep network training by reducing internal covariate shift. arXiv preprint arXiv:1502.03167, 2015.
[5] WAI, Yap June, et al. Fixed point implementation of tiny-yolo-v2 using opencl on fpga. International Journal of Advanced Computer Science and Applications, 2018, 9.10: 506-512.
[6] GE, Jiexian, et al. BNReLU: Combine Batch Normalization and Rectified Linear Unit to Reduce Hardware Overhead. In: 2019 IEEE 13th International Conference on ASIC (ASICON). IEEE, 2019. p. 1-4.
[7] WU, Shuang, et al. L1-Norm batch normalization for efficient training of deep neural networks. IEEE transactions on neural networks and learning systems, 2018, 30.7: 2043-2051.
[8] ZHIJIE, Yang, et al. Bactran: A Hardware Batch Normalization Implementation for CNN Training Engine. IEEE Embedded Systems Letters, 2020.
[9] JUNG, Wonkyung, et al. Restructuring batch normalization to accelerate CNN training. arXiv preprint arXiv:1807.01702, 2018.
Result